## Slide 1: 10/31/18 FREAKLY Meeting Update
Goals**, Problems, and Progress
**GHOULS

## Slide 2: Goals
Goal for this prototype/this semester:
  Wake up system & transmit based on power availability
    Power system will communicate to MSP430 when it is allowed to wake up the Bluetooth chip and transmit.
    The MSP430 will decide whether to take the power system up on that offer.
    If it does, it will power up the Bluetooth module, connect, TX data (not meaningful at this point) to aggregator, and then power down.
  Acquire and store sensor data
    If we get this early enough, integrate with Goal (a) to TX sensor data
  Documentation & planning
    Measure system performance & power consumption enough to set semester 2 goals
Notes: 1.58 = 3e-6*86400*365/60

## Slide 3: Power of Terror!!!
Goal:
  Charge battery using EH IC - DONE
  Monitor power availability
    How?
      Will talk to Erik Welsh
      The PMIC can probably do that
  What voltages y’all want?
    At the moment, I intend on using a regulator (PMIC) to keep a constant 3.3V

## Slide 5: Solar Cell Short Circuit Current
Lamp is comparable to sunlight at 5:00pm
Current at noon ~66% of datasheet value

## Slide 6: Communications
Goal
  Wake and turn off based on power system
  Connect and TX data to phone - DONE
  Determine total power consumption per transmission
    Peak current draw: 180mV/15ohm = 12 mA*
    Avg. current draw while actively transmitting data: 68mV/15ohm = 4.5 mA
    Time: ~6ms to transmit 10 data bits @ avg. current draw
    Wakeup time/current: Complicated due to flaw below, upper bounds probably: < 4 seconds, ~2mA avg. ish, maybe?
Key Flaw: The Bluefruit module can only operate in peripheral mode:
  Cannot initiate connections to other devices.
  This won’t work for chaining nodes together
  Team Decision: Go ahead with this module anyway for now. Will only transition to something else if it seems reasonable to implement.

## Slide 8: Sensor
Goal:
  Be able to acquire data
  Store data to FRAM - DONE
I2C is still being problematic
Have demo I2C code and separate code for this sensor → need to compare them to find our issue