## Slide 1: 11/7/18 Meeting Update
Hoping the turtle really wins the race

## Slide 2: General
Power:
  (1) Have data
  (2) Have researched converters, LDOs, and fuel gauges
Comms:
  (1) Bluefruit BLE generally working
Sensor:
  (1) Have I2C working for temp/humidity sensor
  (2) Have current measurements for sensor

## Slide 3: Power
Data- We have unaliased data, but can’t really filter, the max values are the important ones.
  Current into battery is >5mA in lamplight
  Battery charges quickly, then linearly
  Data presented is over about 8 hours. Getting to 4.2 V will require a lot of data or sunlight
Plans- BQ27426 (Fuel Gauge), TPS6303x (Buck-Boost Converter), LDOs (BH33M0AWHFV-TR , MAX664ESA+)
  Fuel Gauge communicates with MSP
  Buck-Boost converters create a 3.4V line and a 5.1V line
  LDOs bring those lines down to a much cleaner 3.3V and 5V
Our hope is to have parts in and a prototype system kinda working by next weekend

## Slide 4: Power

## Slide 5: Sensor - Coding
Temperature/humidity sensor
  I2C up and working - viewed data and clock lines on oscilloscope
    Byte 1: Device address and read bit (0x40 and a 1)
    Bytes 2-3: Temperature value (came out as 23℃)
    Bytes 4-5: Humidity value (63%)
Next up:
  Save data to FRAM
  Transition from polling to interrupts

## Slide 6: Sensor - Power performance
t1
t2
peak
 | Current (uA)
Avg (over 40ms) | 66
Peak | 528
t1 | 176
t2 | 144
I2C Polling
Measured over 1kΩ resistor

## Slide 7: Next time on CharIoT
System diagram
  Prep for 1st prototype rollout
  Include data flow, power lines, and control signals
Sensor
  Trigger data acquisition using timer
  I2C polling → interrupt based (utilizing low power modes)
  Save data to FRAM
Bluetooth
  TX based on external pin enable (this will come from fuel gauge reading)
Power
  Order Buck Boost converters & LDOs to provide power rails
  Order fuel gauge to provide system monitoring
Notes: 1.58 = 3e-6*86400*365/60