## Slide 1: 9/26/18 Weekly Meeting Update
Documentation, Logistics, New Application

## Slide 2: Agenda
Documentation Drafts
  Look at proposed schedule in Mission Statement
Logistical Questions:
  What is the budget? How do we get access to it?
  Do we need a cover letter as mentioned in the Mission Statement examples?
Research
  Ordering parts for testing
  Talked to Gene about power & Ray about processors
New Application

## Slide 3: Research Update
Comms
  Tested the current draw of the LoRa equipment on hand
Processors
  MSP430 is probably on its way out → not recommended for new designs
    New MSP432 has an ARM M4F core
  ARM cores good because same instruction set → code portability & flexibility
    M4F has more than we probably need so put that on the back burner for now
    Interested in:
      Microchip Atmel SAM L10 (ARM M23 - reduced memory, lower power)
      Microchip Atmel SAM L21 (ARM M0+ - more memory, slightly higher power)

## Slide 4: Processors
 | TI MSP432 (ARM M4F) | TI MSP430 with LEA, 16-bit RISC (ultrasonic) | TI MSP430, 16-bit RISC (value line) | Microchip SAM L10 (ARM M23) | Microchip SAM L21 (ARM M0+)
Power (µA/MHz) | 100 | 118-120 | 81.4-142 | 25 | 35
DMIPS/MHz | 1.25 (1.27 w/FPU) |  |  | 0.98 | 0.95
SRAM | 32-256 KB | Up to 8 KB | 0.5-8 KB | Up to 16 KB | 4-40 KB
Flash | 128-2048 | 128-256 KB FRAM | 0.5-256 KB FRAM | Up to 64 KB | 32-256 KB
GPIO | 48-84 | 68-80 | 12-83 |  | Up to 51
CPU (MHz) | Up to 48 | Up to 16 | Up to 24 | Up to 32 | Up to 48
Notes: Atmel SAM L21 Family
Analog Devices M4F
FPU = Floating Point Unit

## Slide 5: Solar Cells
Maximum power point of solar cells ~70-80% of Voc
Brady and Rachel met with Gene to discuss power
  Gene’s top concerns: 1) Interfacing power, processing, & sensing 2) operating system
  Ultra low power goal cannot be met if we use LoRa and try to meet Flood team’s constraints
  Modularity & general purpose is key
 | KXOB22-12X1F | KXOB22-04X3F | SLMD121H04L | SLMD121H09L | SLMD481H08L
Voc (V) | .63 | 1.89 | 2.52 | 4.5 | 5.04
Isc (mA) | 50 | 15 | 50 | 50 | 178
Power (mW) | -- | -- | 89 | 201 | 714
Size (mm) | 7 x 22 x 1.8 | 7 x 22 x 1.8 | 43 x 14 x 2 | 62 x 21 | 89 x 55 x 2

## Slide 6: Power Storage
First prototype
  Illinois Capacitor Rechargeable Li-Ion Coin Batteries
  Waiting on an email from TI employee so I can pick an EH IC
Future prototypes
  Depends on transmission/processor/sensor methodology choices
  LoRa- Will need a larger battery
  BLE- SSB might be a possibiliy
    Zpower?

## Slide 7: Flood Team
Found that floud team sensor is drawing only 25mA
  However, they have not done range testing yet
Flood team sensor is analog

## Slide 8: Device Application
Flood team PM told us we should aim for a compatible device, not a replacement
  How can we best help the flood project? Scope does not match theirs
Smart Agriculture
  Green Houses
  Hydroponics
  Micro-vintage soil monitoring
Rice Facilities, Engineering, & Planning (FE&P)
  Jones solar panel monitor
  Green Roofs (South Plant, OEDK, Duncan, Mcmurtry have 11,000 sq. ft. of green roof)
http://www.libelium.com/resources/top_50_iot_sensor_applications_ranking/